## Slide 1: Computational Storage: Big Confusion Around a Simple Idea
Tong Zhang
Chief Scientist @ ScaleFlux, Professor @ RPI

## Slide 2: Beautifully Simple Rationale, But …
An active research topic in academia for over 20 years, especially in the past 10 years
Hundreds of millions of dollars of R&D investment over the past ~5 years
CPU
DRAM
DRAM
SSD
CPU
DRAM
DRAM
CSD
Higher performance
Lower power
Lower cost
Papers only

## Slide 3: Beautifully Simple Rationale, But …
CPU
DRAM
DRAM
SSD
CPU
DRAM
DRAM
CSD
Any fundamental flaws here?
Does this idea really make sense?
Is it just another academic fantasy like many others?
Applications
VFS
File system
Block layer
Driver
Computational storage drive (CSD)
POSIX
NVMe
OS
 Very high abstraction-breaking cost

## Slide 4: Beautifully Simple Rationale, But …
CPU
DRAM
DRAM
SSD
CPU
DRAM
DRAM
CSD
Any fundamental flaws here?
Does this idea really make sense?
Is it just another academic fantasy like many others?
Ambiguous & fragmented benefit proposition
Benefit
Cost
Very high abstraction-breaking cost
AI/ML
RDBMs
Block Chain
NLP
Compress
Video
Search
EC
RSA

## Slide 5: Computational Storage
Higher abstraction-breaking cost
Ambiguous & fragmented benefit proposition
Benefit
Cost
Why you guys still try to commercialize computational storage today?
Not necessarily an inherent problem of computation storage!
Conventional computation offloading only mindset

## Slide 6: “Computation Offloading Only” Mindset
SmartNIC
GPU
Video codec
FPGA
TPU
Computation offloading
Applications
VFS
File system
Block layer
Driver
Computational storage drive (CSD)
POSIX
NVMe
OS
Drop the “computation offloading only” mindset?

## Slide 7: Drop the “Computation Offloading Only” Mindset
Applications
VFS
File system
Block layer
Driver
Computational storage drive (CSD)
POSIX
NVMe
OS
Native in-storage computation
Transparent
Abstraction-breaking cost
Ambiguous & fragmented benefit proposition
Wide applicability
Low efficiency of CPU-based implementation
Lossless data compression
Computation function

## Slide 8: Computational Storage
Per-4KB compression
Encryption
TLC/QLC
NAND Flash
Per-4KB decompression
Decryption
Auxiliary fabric (e.g., ARM, RISC-V)
NVMe
Flash Control
SoC
Storage Media
Computational Storage Drive (CSD)
Native in-storage transparent compression (& encryption)
Host-side Driver
Benefit
Cost
Higher abstraction-breaking cost
Ambiguous & fragmented benefit proposition
Cost
Benefit

## Slide 9: Benefit of In-storage Transparent Compression
Transparently reduce the data storage cost
Transparently improve storage IOPS performance
Big but largely unexplored software innovation design space

## Slide 10: Where Does the Innovation Potential Come From?
Data
0’s
4KB
Transparent compression
Compressed data
Unnecessary to completely fill each 4KB sector with user data
User Data
4KB
fixed-size block I/O
Data Management SW
4KB
Data
0’s
Arbitrary data size
Virtually variable-size block I/O

## Slide 11: Software Innovations Enabled by Transparent Compression
Applications
VFS
File system
Block layer
Driver
POSIX
NVMe
OS
CSD
Unchanged
Stage 1
Zero App modification
Stage 2
Modest App modification
Stage 3
Ground-up App development
Entire Design Space
Modify B-tree to reduce write amplification by 10x
A table-less hash-based key-value store

## Slide 12: Computational Storage Drive
Computational Storage Drive
(CSD)
NAND Flash Memory
Transparent compression
+ SSD controller
Now: Xilinx FPGA (UltraScale)  2022: ScaleFlux SoC
Thousands of drives already shipped to customers world-wide!
Notes: Our computational storage drive has a standard U.2 form factor, just like normal NVMe SSD. It integrates TBs of 3D NAND flash memory and a single chip that is responsible for both flash control and computation. Our current product use a single Xilinx FPGA, and later this month we will tape out a 16nm SoC that will power our next-generation product.

## Slide 13: Computational Storage Drive
Transparent compression is of course NOT ALL about computational storage
The best way to commence the journey of commercializing computational storage
Computational Storage
5+ years
Heterogeneity-ready SW/HW ecosystem
5.0/6.0
Notes: Our computational storage drive has a standard U.2 form factor, just like normal NVMe SSD. It integrates TBs of 3D NAND flash memory and a single chip that is responsible for both flash control and computation. Our current product use a single Xilinx FPGA, and later this month we will tape out a 16nm SoC that will power our next-generation product.

## Slide 14: The Next Step
CSD Ctrl SoC
(w/ trans. comp.)
NAND Flash
4~8GB/s
CSD Ctrl SoC
(w/ trans. comp.)
NAND Flash
4~8GB/s
PCIe (16~32GB/s)
OS
Computational Storage Drive (CSD)
CSD Ctrl SoC
(w/ trans. comp.)
NAND Flash
4~8GB/s
I/O stack
Applications
PCIe (16~32GB/s)
Computational Storage Drive (CSD)
I/O stack
Accel.
PCIe (16~32GB/s)
Computational Storage Drive (CSD)
I/O stack
. . .
. . .
Accel.
Accel.
Well aligned with CXL and chiplet technology
Parasitic accelerator
 Parasitic computation offloading without changing I/O stack

## Slide 15: Ultimate Computational Storage
CSD Ctrl SoC
(w/ trans. comp.)
NAND Flash
4~8GB/s
CSD Ctrl SoC
(w/ trans. comp.)
NAND Flash
4~8GB/s
PCIe (16~32GB/s)
OS
Computational Storage Drive (CSD)
CSD Ctrl SoC
(w/ trans. comp.)
NAND Flash
4~8GB/s
I/O stack
Applications
PCIe (16~32GB/s)
Computational Storage Drive (CSD)
I/O stack
Accel.
PCIe (16~32GB/s)
Computational Storage Drive (CSD)
I/O stack
. . .
. . .
Accel.
Accel.
High abstraction-breaking cost
Accel.
Accel.
Accel.
Parasitic acceleration
I/O-path acceleration
Transparent computation
Computational Storage
Heterogeneity-ready SW/HW ecosystem

## Slide 16: Conclusion
Computation offloading
Break the principle of abstraction
Heterogenous Computing
SmartNIC
GPU
Video codec
DPU
TPU
CSD
Higher abstraction-breaking cost
Ambiguous benefit proposition
Evolutionary Path
Transparent Computation
Phase 2
Transparent/Parasitic Computation
Phase 3
Transparent/Integrated Computation
Parasitic Accel.
Parasitic & I/O-path Accel.
Chiplet technology is the key