## Slide 1: NEOCLOUD REDFISH
OCP GLOBAL SUMMIT 2026 · SCALING AI CLUSTERS AT NEOCLOUDS
An evidence-based out-of-band management profile for GPU fleets
Jonmichael Hands · FarmGPU · Chair, OCP neocloud workstream
Draft v0.6.0 · not an approved OCP profile
MEASURED IN PRODUCTION
153
BMCs at two sites
3
server platforms, two OEMs
148k
active series, zero probe errors
Notes: Intro. I chair the OCP neocloud workstream (Scaling AI Clusters at Neoclouds). This is the Neocloud Redfish profile family, draft v0.6.0, developed in opencomputeproject/neocloud-redfish. It is a draft for the workstream and the Hardware Management Profiles workstream, not an approved OCP profile. The headline: every requirement is backed by measurements from production fleets, not datasheets. The numbers on the right are from 2026-09-20: 153 BMCs across two sites and three server platforms, about 148k active series, zero probe errors. Site and node names are anonymized throughout.

## Slide 2: HARDWARE YOU DIDN'T DESIGN
BACKGROUND
A neocloud rents GPU servers it did not design, from several OEMs, to tenants whose operating systems it often cannot touch.
The only management surface guaranteed on every node is the BMC. This profile says what that surface must expose for agentless, read-only fleet health at ClusterMAX Reliability & Monitoring grade.
Several OEMs per fleet
Each models the GPU tray its own way
No in-band on tenant nodes
No host agent, no DCGM, no OS logs once rented
The BMC is the floor
Agentless, GET-only, one read-only credential
NEOCLOUD REDFISH PROFILE · DRAFT V0.6.0
02
Notes: The neocloud operating model is the reason for a separate profile. We run servers from several OEMs, we didn't design them, and once a node is rented the tenant owns the OS, so there's no host agent, no DCGM, no OS logs. The BMC is the one surface we always have. The question this profile answers: what must the BMC expose so an operator can do fleet health at ClusterMAX Reliability and Monitoring grade, agentless, GET-only, with a read-only credential.

## Slide 3: OPERATORS RANKED THIS FIRST
BACKGROUND
#1
Hardware management & interop — BMC, BIOS, firmware, telemetry — ranked first on importance and on OCP leverage in the workstream's March 2026 operator survey.
The ask
An interoperability checklist, plus gap tickets into the OCP Hardware Management project.
The deliverable
That checklist in machine-validatable form: a DSP0272 Redfish Interoperability Profile family.
The baseline gap
UBB 2.0.0 asks MemoryMetrics for BandwidthPercent only, PortMetrics for RX/TX bytes. No RAS content.
NEOCLOUD REDFISH PROFILE · DRAFT V0.6.0
03
Notes: Why OCP, why now. In the March 2026 survey of the Scaling AI Clusters at Neoclouds workstream, hardware management and interop ranked number one on both importance and on how much leverage OCP has. The survey named the deliverable: an interoperability checklist plus gap tickets into the Hardware Management project. This repo is that checklist, written as a Redfish Interoperability Profile so a machine can check it. The gap it fills: the existing GPU baseline, OCP_UBB_BaselineManagement 2.0.0, requires only BandwidthPercent from MemoryMetrics and RX/TX bytes from PortMetrics. No ECC, no row remap, no link errors, nothing an operator alerts on.

## Slide 4: FOUR DESIGN CHOICES
BACKGROUND
01
Every rule cites evidence
[live] fleet queries · [rec] recorded BMC trees · [sweep] a 259-address unauthenticated sweep. Nothing from datasheets.
02
Testable without hardware
Recorded trees in DMTF mockup layout, checked by the DMTF Interop Validator. CI checks every profile against DSP0272.
03
Composes, doesn't re-specify
RequiredProfiles pulls in approved OCP baselines and UBB 2.0.0. This family adds only what neoclouds need.
04
Two surfaces, two levels
Host BMC and accelerator controller profiled separately. Core = Mandatory floor; Trusted = Recommended, for contracts.
NEOCLOUD REDFISH PROFILE · DRAFT V0.6.0
04
Notes: Four things make this different from a typical profile. One: every requirement carries an evidence tag. [live] is a Thanos query against two production sites on 2026-09-20; [rec] is a recorded BMC tree committed as a test fixture; [sweep] is an unauthenticated sweep of 259 BMC addresses. Two: you can test it with no hardware: recordings in DMTF mockup layout are served by the DMTF Redfish-Mockup-Server and checked by the DMTF Redfish-Interop-Validator. Three: it composes the approved OCP Service Baseline, Baseline Hardware Management and Server profiles and the System GPU Management workstream's UBB 2.0.0 rather than restating them. Four: the host BMC and the accelerator controller are profiled separately, at two levels: Neocloud-Core is Mandatory, Neocloud-Trusted is Recommended and meant for contracts.

## Slide 5: SURVEY TO FLEET EVIDENCE
PROGRESS
MAR 2026
Operator survey
HW management & interop ranked #1 by workstream members
AUG 2026
v0.5.0 draft
Reasoned from the standards, in a fork of the OCP profiles repo
AUG 13
Repo created
neocloud-redfish under the OCP GitHub org
AUG – SEP
Fleet collection
Exporter 1.0.0 on 153 BMCs; three BMC trees recorded
SEP 20
v0.6.0 draft
Three-profile family rebuilt on fleet evidence
OCT 12–15
OCP Global Summit
DMTF proposals and a call for validation runs
v0.5.0 reasoned from the standards. v0.6.0 is what six weeks of production collection changed.
NEOCLOUD REDFISH PROFILE · DRAFT V0.6.0
05
Notes: Timeline. The March survey set the priority. The v0.5.0 draft in August reasoned from the standards and vendor docs, developed in a fork of HWMgmt-OCP-Profiles on a neocloud-profiles branch. The repo opencomputeproject/neocloud-redfish was created August 13. Then the collector the draft described actually shipped: the reference exporter 1.0.0 has run continuously against 153 BMCs at two sites, and three BMC trees were recorded as fixtures (a healthy Supermicro HGX B200, the same SKU with its tray detached, and a Dell XE9680). v0.6.0 on September 20 is the rebuild on that evidence. Today at the Summit we bring the DMTF proposals and ask other operators to run the validator.

## Slide 6: MEASURED ON PRODUCTION FLEETS
PROGRESS
153
BMCs across two sites
3
server platforms, two OEMs
148k
active series in Thanos
0
probe errors on any fleet
Fleet | Platform | BMCs | OOB coverage | Series/node | Probe p50
Site A · A1 | Supermicro HGX B200 | 128 | 128/128 BMC · 127/128 HMC | 996 | 1.7 s
Site B · B1 | Supermicro HGX B200 | 15 | 15/15 · 14 days continuous | 1,062 | 1.8 s
Site B · B2 | Dell XE9680 H100 · iDRAC9 7.20 | 10 | 10/10 · no HMC by design | 432 | 6.7 s
Source: Thanos PromQL at both sites, 2026-09-20 · GET-only exporter, read-only BMC accounts
06
Notes: What we measured on 2026-09-20. Every number is a PromQL result, not an estimate. Site A fleet A1: 128 Supermicro HGX B200 nodes, 128 of 128 BMCs and 127 of 128 HMCs up, 10 days continuous, about 1,000 series per node, 1.7 second median probe. Site B: 15 more Supermicro B200 nodes and 10 Dell XE9680 H100 nodes on iDRAC9 7.20. Dell has no HMC surface by design, and its probe is 4x slower because iDRAC advertises $expand MaxLevels 1, so the exporter walks 8 GPUs resource by resource. Supermicro advertises MaxLevels 3 plus excerpt and $select. Active series: 127,734 at Site A, 20,245 at Site B. Zero probe errors.

## Slide 7: FOUND OUT-OF-BAND, NO HOST AGENT
PROGRESS
1
HGX tray detached: host off, 0/34 parts
13
dead PSUs on 11 nodes, 8 in one rack
9
GPUs at 0 PCIe lanes, still Enabled/OK
2
GPUs with no HBM row-remap capacity left
1
GPU with lifetime uncorrectable HBM ECC
978
lifetime NVSwitch link-downs, one switch
3
HMC firmware bands mid-rollout
555
kW chassis power visible OOB at Site A
Live alerts and fleet state, 2026-09-20 · every signal from the profile's Mandatory set
07
Notes: What the Mandatory set surfaced on one evening, with no host agent. One HGX tray detached: host off, zero of 34 accelerator components. 13 dead power supplies on 11 nodes, drawing about 5 W input; 8 of them in one rack, which points to a feed or PDU problem rather than 8 coincident PSU failures. 9 GPUs at zero PCIe lanes on 2 nodes, the fell-off-the-bus signature, while Redfish still reports them Enabled and OK. 2 GPUs with no HBM row-remap capacity left: RMA candidates before a double-bit error. 1 GPU with lifetime uncorrectable HBM ECC. NVSwitch unintentional link-down counters up to 978 per switch, lifetime counters, so useful as increase(). Three HMC firmware bands in production at once, which changes the tree shape: 34 firmware components on 25.05 and 26.04, 25 on 25.02. And 555.5 kW of chassis power, 309.7 kW of it GPU tray, visible fleet-wide out of band.

## Slide 8: THE FAILURE EVERY PATH MISSED
PROGRESS
AUG 2026 · NODE A1-69
9 days
Undetected. The BMC stayed healthy while the HGX tray answered HTTP 503 on every path.
SEP 18, 2026 · NODE A1-17
5 min
Caught by out-of-band liveness: host off, 0 of 34 accelerator components answering.
Accelerator-subsystem liveness is now a Core item: subordinate Manager.Status.State, a FirmwareInventory census, and an AcceleratorSubsystemUnavailable message.
NEOCLOUD REDFISH PROFILE · DRAFT V0.6.0
08
Notes: The story that changed the design most. In August, node A1-69 lost its HGX tray. The host BMC kept answering, redfish_up stayed 1, and every HGX path returned 503. Nothing in any other monitoring path noticed for nine days. On September 18 the same signature hit A1-17: Chassis members dropped from 39 to 3, FirmwareInventory from 66 to 19, HGX members 34 to 0. This time the exporter caught it in five minutes. Two detached trays in six weeks, both invisible to everything else. So liveness of the accelerator subsystem is now a first-class conformance item: the subordinate Manager must report Status.State, FirmwareInventory must enumerate every accelerator component so a drop is visible, and the draft OCPAcceleratorRAS registry defines AcceleratorSubsystemUnavailable and Restored. We are also asking DMTF to clarify this in DSP2090, the aggregation guidance.

## Slide 9: VALIDATOR RUNS ON REAL BMC TREES
PROGRESS
Profile · BMC | Pass | Fail | Not tested
Platform · Dell | 675 | 40 | 78
Platform · Supermicro | 48 | 25 | 26
Accelerator · Dell | 7,107 | 93 | 98
Accelerator · Supermicro | 54 | 47 | 22
DMTF Redfish-Interop-Validator 3.0.0 · composed profile tree · --nooemcheck
Read the fails right
Most are resources the recording never fetched. Property-level fails are few, and real.
7 upstream defects
Found while validating. Two abort every run: a UBB 2.0.0 typo and a validator UseCaseType crash.
NEOCLOUD REDFISH PROFILE · DRAFT V0.6.0
09
Notes: The profiles run against real recorded responses with no hardware. Read these numbers with the recording's scope in mind: a resource the collector never fetched shows as not found, which is not the same as absent from the BMC. The property-level fails on recorded resources are few and real. Dell: MultipleHTTPRequests, UUID, Chassis.Controls, the Intake thermal context, serial-console types, and the LogServices link on the GPU system. Supermicro: MultipleHTTPRequests. On Dell's Accelerator run, 15 property-level fails, 8 of them UBB 2.0.0 items. Validating also exposed 7 defects upstream: Server 1.0.0 declares ProfileVersion "1,0,0"; Baseline 1.1.1 self-declares 1.1.0; Server 1.0.0 assumes Intake thermal context and SSH/IPMI serial console; the HWMgmt-OCP-Profiles README cites DSP0272 1.4.0; the System GPU spec links UBB at its old path; UBB 2.0.0 has IfImplement and HTTP?? typos that abort the validator; and validator 3.0.0 calls get_resource_data instead of get_resource for UseCaseType, which crashes any profile using ProcessorType UseCases. Our CI carries a one-word workaround.

## Slide 10: TWO SURFACES FAIL INDEPENDENTLY
ARCHITECTURE
Host BMC · Platform
DMTF-standard Redfish on every vendor: power, thermal, drives, DIMMs, CPUs.
GPU HMC · Accelerator
NVIDIA HMC on the HGX baseboard: GPUs, HBM, NVLink. Reachable only if the BMC aggregates it.
 | Supermicro HGX B200 | Dell XE9680 · iDRAC9 | Lenovo SR680a V3 · XCC
Platform tier | Pass | Pass | Pass
Accelerator surface | HMC aggregated | Own GPU model, OEM props | Temp & power only
HBM ECC (LifeTime) | Present | Absent | No surface
NVLink as Port | 19 per GPU | Oem.Dell only | No surface
$expand MaxLevels | 3 · 1.7 s per node | 1 · 6.7 s per node | Not measured
NEOCLOUD REDFISH PROFILE · DRAFT V0.6.0
10
Notes: The core architectural finding. There are two management surfaces on a GPU server and the fleet shows they behave differently. The host BMC speaks standard DMTF Redfish on every vendor. The accelerator side is the NVIDIA HMC on the HGX baseboard, and its content is consistent, but its reachability isn't. Supermicro aggregates the HMC natively: 12 HGX bulk MetricReports, 14 of 15 standard ProcessorMetrics paths, HBM LifeTime ECC. Dell iDRAC9 7.20 models the GPUs itself with Oem.Dell and Oem.Nvidia properties, no HBM ECC, and NVLink only as OEM properties rather than Port resources. Lenovo XCC exposes GPU temperature and power and nothing else. A single flat GPU server profile can't be Mandatory-satisfiable across all three, so the host tier and the accelerator tier are separate profiles. That way each vendor's gap is legible instead of one red fail.

## Slide 11: COMPOSED FROM APPROVED OCP WORK
ARCHITECTURE
Neocloud Accelerator
0.6.0 · GPU tier, new
Neocloud Platform
0.6.0 · host tier, new
OCP UBB Baseline
2.0.0 · System GPU Mgmt
Neocloud ServiceCore
0.6.0 · service plane, new
OCP Service Baseline
1.0.0 · approved
OCP Baseline HW Mgmt
1.1.0 · approved
OCP Server HW Mgmt
1.0.0 · approved
Arrows = RequiredProfiles · GPU node = Platform + Accelerator · CPU or storage node = Platform alone
11
Notes: How the family composes. Three new files, in green. Accelerator requires ServiceCore and the System GPU Management workstream's OCP_UBB_BaselineManagement 2.0.0, which is being renamed MAS. Platform requires ServiceCore. ServiceCore requires the three approved OCP profiles: Service Baseline 1.0.0, Baseline Hardware Management 1.1.0, and Server Hardware Management 1.0.0 (1.1.0 is awaiting promotion). A GPU node conforms to Platform plus Accelerator, which pulls in everything transitively. A CPU or storage node conforms to Platform alone. The validator merges required profiles and applies the strictest requirement per property, so one run tests the whole tree. Accelerator requirements are scoped with UseCases on ProcessorType so they don't get applied to CPU sockets, which is exactly what happened in v0.5.0.

## Slide 12: WHAT EACH PROFILE REQUIRES
ARCHITECTURE
Profile | Neocloud-Core · Mandatory | Neocloud-Trusted · Recommended
ServiceCore | Pre-auth identity · $expand MaxLevels · subordinate Manager.Status.State · full accelerator FirmwareInventory · EventService · ReadOnly role · audit log | SSE streaming · VendorCode/CPER · Status.Conditions · SPDM attestation · SecureBoot · MFA/OAuth2
Platform | PowerState · PSU status incl. Absent bays, in/out watts · thermal & fans · Drive.FailurePredicted · DIMM/CPU health · containment | Energy metrics · Sensor thresholds · NVMe SMART where present
Accelerator | ProcessorMetrics with PCIe AER and LanesInUse · HBM LifeTime ECC · temp & power · NVLink Port status, speed, errors · accelerator Manager | Throttle durations · cache ECC · Switch/Fabric · per-value timestamps · RAS registry MessageIds
Plus a draft OCPAcceleratorRAS 1.0.0 registry — 13 messages: subsystem unavailable/restored, XID and SXID, HBM ECC, row remap pending/failed/exhausted, fell off bus, PCIe link degraded, sustained throttle, stale metric.
NEOCLOUD REDFISH PROFILE · DRAFT V0.6.0
12
Notes: Two levels, expressed with ReadRequirement. Neocloud-Core is Mandatory: the floor for onboarding a fleet for agentless health. Direct-GET telemetry only, no telemetry license, no writes. Neocloud-Trusted is Recommended: what an operator asks for in a contract. ServiceCore adds pre-auth identity, $expand MaxLevels (value guidance at least 2, because MaxLevels 1 costs 4x per node), subordinate Manager state for tray liveness, a FirmwareInventory census, EventService, a provably ReadOnly role for the monitoring credential, and the audit log. Platform adds PSU semantics where an empty bay reports Absent rather than failed, Drive.FailurePredicted, DIMM and CPU health and containment links for power scope. Accelerator is UseCase-scoped to GPU processors: PCIe AER and LanesInUse, which is the bus-drop signal, HBM LifeTime ECC, NVLink port health. Things nothing in the fleet implements, like MemoryMetrics CurrentPeriod and HealthData, were demoted to Recommended. Today Platform Core passes on Supermicro, Dell and Lenovo; Accelerator Core passes on Supermicro HGX. No BMC in the fleet populates Status.Conditions yet.

## Slide 13: EVERY REQUIREMENT HAS EVIDENCE
ARCHITECTURE
[live]
153 BMCs, two sites, three platforms
GET-only exporter, read-only accounts
Alloy to Thanos; every number a PromQL result
[rec]
BMC trees recorded, identities redacted
Served in DMTF mockup layout
DMTF Mockup Server + Interop Validator 3.0.0
[sweep]
259 BMC addresses, no credentials
Unauthenticated service-root GETs
121 of 121 BMCs identified before login
CI on every push: build_profiles.py regenerates the JSON, every profile is checked against the DSP0272 schema, and each requirement's Purpose carries its evidence tag.
NEOCLOUD REDFISH PROFILE · DRAFT V0.6.0
13
Notes: How the evidence stays attached. Three sources. Live: an agentless, GET-only Redfish exporter with read-only credentials on 153 BMCs, scraped by Grafana Alloy into Thanos; every number in this talk is a PromQL result. Recorded: BMC trees recorded GET-only with identities redacted and every metric value and firmware string kept, laid out as DMTF mockups so the DMTF Mockup Server can serve them and the Interop Validator can run against real responses with no hardware and no credential. Sweep: an unauthenticated sweep of 259 addresses; 121 of 121 BMCs were uniquely identified before login, which is why pre-auth identity is a requirement. In the repo, build_profiles.py is the source and generates the JSON; CI regenerates it, checks every profile and every composed upstream profile against the DSP0272 schema, and smoke-runs the validator. Each requirement's Purpose text carries its [live], [rec] or [sweep] tag. The recordings will be published once a second unit per platform is recorded.

## Slide 14: TAKING OEM COUNTERS TO DMTF
NEXT STEPS
Signal the fleet alerts on | Where it lives today | Proposed standard carrier
Accelerator tray liveness | HTTP 503 on the subtree | Subordinate Manager.Status.State + event (DSP2090)
HBM row remapping | MemoryMetrics.Oem.Nvidia | MemoryMetrics.RowRemapping: counts, pending, banks
Scale-up link errors | PortMetrics.Oem.Nvidia | PortMetrics link-down, BER, symbol-error counters
Throttle reasons | ProcessorMetrics.Oem.Nvidia | ProcessorMetrics.ThrottleReasons[] + durations
Stale metric values | Oem.Nvidia.MetricValueStale | MetricValue.Stale, or a required per-value Timestamp
XID / SXID codes | Free text in log messages | VendorCode (Redfish 2026.2) + OCP RAS registry
Schema items go through the OCP HM Profiles call, where DMTF co-authors. Registry items go to System GPU Management, where NVIDIA co-leads.
NEOCLOUD REDFISH PROFILE · DRAFT V0.6.0
14
Notes: The counters that carry the fleet's real RAS load have no standard home; they all live in Oem.Nvidia. These are the top six of twelve proposals in docs/dmtf-proposals.md, ordered by operational weight. One: tray liveness, an aggregated subordinate Manager should report UnavailableOffline and emit a presence-mismatch-class or AcceleratorSubsystemUnavailable event, clarified in DSP2090. Two: HBM row remapping, ten GPUs with remaps and two with no capacity left; propose a MemoryMetrics.RowRemapping block with counts, pending, failed and bank availability. Three: scale-up link counters, link downed, unintentional link down, recovery, symbol errors, effective BER; Port already has PortProtocol NVLink, UALink and UET. Four: throttle reasons as an enum mirroring DCGM clock-event reasons, plus violation durations. Five: per-value staleness in MetricReports; we drop 11 stale values per fleet scrape. Six: XID and SXID use the new VendorCode field from Redfish 2026.2 with a neutral MessageId from an OCP accelerator RAS registry. Mike Raineri at DMTF co-authors the OCP profiles, so schema items come through the HM Profiles call first.

## Slide 15: WHAT WE ASK EACH VENDOR
NEXT STEPS
Dell
Today: Platform pass · Accelerator fail
HBM ECC and NVLink Ports over Redfish on iDRAC9. iDRAC10's GPU Statistics report suggests the data exists.
Lenovo
Today: Platform pass · no accelerator surface
Aggregate the HGX HMC on the SR680a V3, an HGX H200 system shipping without the HGX Redfish tree.
NVIDIA
Today: HMC content passes Core
Fix the LinkStatus enum (reads "OK"), report HMC Manager.Status.State on tray loss, standardize MetricValueStale.
Supermicro
Today: passes Core on both tiers
Populate Status.Conditions and support MultipleHTTPRequests.
Raised through the OCP HM Profiles call and OEM account teams, Q4 2026
15
Notes: The profile makes each vendor's gap legible, and that's the deliverable, not a defect of the profile. Dell: iDRAC9 7.20 passes Platform and fails Accelerator Core on MemoryMetrics.LifeTime, meaning no HBM ECC over Redfish, and on Processor.Ports. The iDRAC10 telemetry guide documents a GPU Statistics report with SBE and DBE counters, so the data likely exists. Lenovo: the SR680a V3 is an HGX H200 system, but XCC exposes no HMC aggregation, only GPU temperature and power. NVIDIA: LinkStatus on HMC ports reads "OK" instead of LinkUp, the HMC Manager should report Status.State when the tray is lost, and MetricValueStale should become standard. Supermicro passes Core on both tiers today; the asks are Status.Conditions, which no BMC in the fleet populates yet, and MultipleHTTPRequests, which fails the OCP Service Baseline.

## Slide 16: PATH TO AN APPROVED PROFILE
NEXT STEPS
OCT 12–15
At the Summit
DMTF schema proposals: row remap, link counters, throttle reasons, stale flag
Tracking issue in HWMgmt-OCP-Profiles
File the 7 upstream defects
Q4 2026
Co-review
System GPU Management co-reviews the Accelerator profile
RAS messages into their registry; track the UBB-to-MAS rename
Vendor asks to Dell, Lenovo, NVIDIA, Supermicro
THEN
Promotion
Second unit per OEM, plus Gigabyte, ASUS and MSI HGX
Publish recorded trees in DMTF mockup layout
Usage Guide in the OCP template; request promotion
Later: OCPNeocloudRack for NVL72 power and cooling
Venue: OCP Hardware Management, Manageability Profiles workstream · sponsor: FTI neocloud workstream
16
Notes: How this becomes an approved OCP profile. All OCP Redfish profiles are owned by the Hardware Management project's Manageability Profiles workstream; John Leung maintains HWMgmt-OCP-Profiles and Mike Raineri from DMTF co-authors. The FTI neocloud workstream is the sponsor, not the approval body. This week: the DMTF schema proposals, a tracking issue in HWMgmt-OCP-Profiles, and the seven upstream defects. Q4: ask System GPU Management to co-review the Accelerator profile and fold the OCPAcceleratorRAS messages into their registry work (their issue 56), track the UBB-to-MAS rename, and take the vendor asks through the Profiles call and account teams. Then: every recording today is one machine per platform, so we re-run Core on a second unit per OEM and on Gigabyte, ASUS and MSI HGX units, publish the trees, write the Usage Guide in the OCP markdown template, and request promotion once two machines per OEM validate. Rack power and cooling for NVL72 comes later as an OCPNeocloudRack profile once a Redfish-speaking PDU is in the fleet to record.

## Slide 17: THE ASK: VALIDATE YOUR FLEET
NEXT STEPS
Operators
Run the validator on one HGX unit per OEM you operate. File the fails as issues.
OEMs & NVIDIA
Close the named gaps: HBM ECC, NVLink Ports, HMC aggregation, tray liveness.
DMTF & OCP
Co-review the Accelerator profile and the schema and registry proposals.
pip install redfish_interop_validator
rf_interop_validator -r https://<bmc> -u <ro-user> -p <pw> --nooemcheck profiles/OCPNeocloudAccelerator.v0_6_0.json
github.com/opencomputeproject/neocloud-redfish · GET-only, read-only account
Scaling AI Clusters at Neoclouds · opencompute.org/projects/scaling-ai-clusters-at-neoclouds
Notes: The ask. Operators: run the validator against one HGX unit per OEM you operate and file the fails as issues on the repo. We are not asking anyone to adopt our collector; we're asking you to validate your OEMs against the profile. Denvr, Scaleway, Lambda and Crusoe were asked at the workstream; anyone in the room running HGX is welcome. It's GET-only with a read-only account, so it is safe to point at production. OEMs and NVIDIA: the gaps are named on the vendor slide. DMTF and OCP: co-review the Accelerator profile and the schema and registry proposals. Everything is in opencomputeproject/neocloud-redfish under CC-BY-SA-4.0, matching the OCP profile corpus. Thank you; questions.