## Slide 2: Yosemite V2 – Modular 1S Platform
Damien Chong, Hardware Engineer, Facebook
Anthony Chan, Electrical Engineer, Facebook

## Slide 3: Yosemite V2: Modular platform
Intel
x86
Twin Lakes
50Gbps
MH NIC
100Gbps
MH NIC
OpenRack V2
EMI
& Safety
Dual ODM
Hot Service
Intel
x86
Twin Lakes
6x M.2
Glacier Point
PCIe CEM
Crane Flat
M.2

## Slide 4: Yosemite V2: Spec changes
Updating SVR_ID0 / GPIO0 definition to scale the platform supporting more cards.
Old definition |  | New definition | 
< 1.0v | Smart SoC card | < 0.44v | Smart SoC card
 |  | 0.7v +/- 0.25v | Smart device card
1.2v +/- 0.2v | Crane Flat PCIe CEM carrier card | 1.2v +/- 0.25v | Crane Flat PCIe CEM carrier card
1.7v +/- 0.2v | Glacier Point 6x M.2 carrier card | 1.7v +/- 0.25v | Glacier Point 6x M.2 carrier card
BMC ping Bridge-IC on Smart SoC card for identification
BMC read Smart device card I2C address 0xA2 EEPROM for identification

## Slide 5: 1S compute: Twin Lakes
SoC | Intel Skylake-DE 18-cores
Memory | 4-channel 2DPC DDR4 2400
Boot drive | 1x 2280 PCIe Gen3 M.2
Expansion | 2x 22110 PCIe Gen3 M.2
Spec compliance | Twin Lakes 1S OCP spec

## Slide 6: M.2 carrier card: Glacier Point
Glacier Point v1 | 6x PCIe Gen3 22110 form factor
Next generation: Glacier Point v2 in concept | 12x PCIe Gen3 22110 form factor with PCIe switch

## Slide 7: PCIe CEM carrier card: Crane Flat
Crane Flat | Half width full height PCIe x16

## Slide 8: Hot service: Removal card for service only impact individual compute node
Insert the card
Card LED stop blinking
Push-in sled
Trigger service event
BMC out-of-band
USB debug card
Card removal:
Card insertion:
Service event complete
Sled front panel LED blink
Card to be serviced slot LED blink
+
Pull-out sled
Remove the card
Power down card(s)
Power up
card(s)

## Slide 9: Hot service: Enabling from design perspective
High-level goals
  Solution is seamless from operator perspective
  Minimize power loss during normal operation
  Mechanism to prevent cascading failures
Main electrical components
  E-brush connector
  Power bar PCB
Sled pulled out during hot service
Sled pushed in during normal operation

## Slide 10: Hot service: Enabling from design perspective
Underside view of sled
E-brush connector mounted on baseboard
Gold-to-gold contact between e-brush and power bar PCB
Fan latch toggle switch

## Slide 11: Hot service: Enabling from design perspective
Power bar PCB w/ e-fuse protection
Over current protection threshold | ~ 70A
Added power loss (12V @ 50A) | < 2W
Auto retry after fault support | Yes

## Slide 12: Learn More About Yosemite V2
Yosemite V2 OCP specification here
Twin Lakes OCP specification here
Visit the Facebook booth located at A13 to learn more

## Slide 13
Notes: Big picture taking all the slide, with no text